| EMERGENCY PROCEDURES |  | EMERGENCY PROCEDURES |
| --- | --- | --- |
| PA-28-181 ARCHER II |  | PA-28-181 ARCHER II |
| Engine Fire During Start |  | Power-Off Landing |
| Starter -- crank engine |  | Fuel Selector -- OFF |
| Mixture -- idle cut-off |  | Magnetos -- OFF |
| Throttle -- full open |  | Mixture -- idle cut-off |
| Fuel Pump -- OFF |  | Master Switch -- OFF |
| Fuel Selector -- OFF |  | Seatbelts -- secure |
|  |  | Door -- secured open |
| Engine Power Loss: Takeoff |  | Speed -- 63 KTS, flaps 40( |
| Pitch for a safe airspeed |  | Fire In Flight |
| Fuel Selector – switch tanks |  |  |
| Magnetos -- cycle |  | (electrical fire) |
| Primer -- locked |  | Master Switch -- OFF |
| Mixture – full rich |  | Heater -- OFF |
| Fuel Pump --ON |  | Defroster -- OFF |
| Carburetor Heat -- ON |  | Air Vents -- OPEN |
| If no restart, follow POWER-OFF LANDING procedure |  | Land as soon as possible |
| Engine Power Loss: In-Flight |  | (engine fire) |
|  |  | Establish an Emergency Descent |
| Airspeed: 76 KTS, Best Glide airspeed |  | Fuel Selector -- OFF |
| Best Site |  | Primer -locked |
| Checklist: |  | Throttle -- closed |
| Fuel Selector – switch tanks |  | Mixture – idle cut-off |
| Magnetos --cycle |  | Fuel Pump –OFF |
| Primer --locked |  | Carburetor Heat -- OFF |
| Mixture – full rich |  | Cabin Heat -- OFF |
| Fuel Pump --ON |  | Defroster -- OFF |
| Carburetor Heat -- ON |  | Windows / Air Vents -- OPEN |
| Declare: Talk on 121.5; Squawk 7700; ELT -ON |  | Follow POWER-OFF LANDING procedure |
| Evacuate: Follow POWER-OFF LANDING Procedure |  |  |
| EMERGENCY PROCEDURES |  | EMERGENCY PROCEDURES |
| PA-28-181 ARCHER II |  | PA-28-181 ARCHER II |
| Loss Of Fuel Pressure |  | Spin Recovery |
| Fuel Pump -- ON |  | Throttle -- idle |
| Fuel Selector – switch tanks |  | Ailerons -- neutral |
|  |  | Rudder -- full opposite direction of rotation |
| Electrical Failure |  | Control Wheel -- full forward |
|  |  | Rudder -- neutral when rotation stops |
| 1.) ALT light illuminated: |  | Control Wheel -- as required to smoothly regain level flight attitude |
| Ammeter -- check to verify inoperative |  |  |
|  |  | Open Door |
| 2.) If ammeter shows zero: |  |  |
| ALT switch -- OFF |  | Airspeed: slow to 87 KTS |
|  |  | Air Vents -- closed |
| 3.) Reduce electrical loads to a minimum |  | Window -- open |
| ALT circuit breaker -- check and reset |  | If upper latch open -- latch |
| ALT switch -- ON |  | If lower latch open -- pull on arm rest and latch |
|  |  | If both latches open -- latch lower, then upper |
| 4.) If power is not restored: |  |  |
| ALT switch -- OFF |  | Carburetor Icing |
| Land as soon as possible |  | Carburetor Heat -- ON |
|  |  | Mixture -- adjust for max. engine smoothness |
| Electrical Overload |  |  |
| ALT switch -- ON |  | Engine Roughness |
| Battery switch -- OFF |  | Carburetor Heat -- ON |
|  |  | If roughness continues: |
| If alternator loads are reduced: |  | Carburetor Heat -- OFF |
| Electrical load -- reduce to a minimum |  | Mixture -- adjust for max smoothness |
|  |  | Fuel Selector -- switch tanks |
| If alternator loads are not reduced: |  | Magnetos -- cycle |
| ALT switch -- OFF |  | Primer -- locked |
| Battery switch -- as required |  | Fuel Pump -- ON |
| Land as soon as possible |  | Engine Gauges – check for abnormal |