PA-28-181 ARCHER II

PREFLIGHT CHECKLIST

| CABIN CHECK | Propeller -CHECK |
| --- | --- |
| Parking Brake -SET | Alternator Belt -CHECK TENSION |
| Pitot-Static Drains -DRAIN | Landing Gear -CHECK |
| Radios and Navigation Equipment -OFF | Fuel Drain (Gascolator) -CLOSED |
| Primary & Secondary Flight Controls -CHECK FULL TRAVEL | Crankcase Breather Line -CHECK |
| ELECTRICAL SYSTEMS | LEFT WING |
| Master Switch -ON | (same as right wing) |
| Turn Coordinator Gyro -SPINNING UP | Pitot-Static Probe -NO BLOCKAGE |
| Fuel Gauges -CHECK INDICATIONS |  |
| Lights and Pitot Heat -ON AND VERIFY FUNCTIONING | LEFT FUSELAGE |
| Stall Warning Horn –CHECK | Windows -CHECK |
| Lights and Pitot Heat–OFF | Side -CHECK |
| Master Switch -OFF | Air Vent -NO BLOCKAGE |
|  | Antennas -CHECK |
| FUEL (sample two main tanks first; fuel strainer LAST) | Bottom -CHECK |
| Quantity –CHECK |  |
| Grade –SAMPLE & VERIFY (4 Samples Total) | EMPENNAGE |
| Quality –SAMPLE & CHECK | Stabilator & Trim Tab -CHECK |
|  | Tailcone -CHECK |
| EXTERIOR CHECK: Flaps –FULLY EXTENDED (40() | Vertical Stabilizer -CHECK |
|  | Rudder -CHECK |
| RIGHT WING | Antennas -CHECK |
| Flaps -CHECK |  |
| Ailerons -CHECK | RIGHT FUSELAGE |
| Wingtip -CHECK | Windows –CHECK |
| Wing Stiffness -CHECK | Side –CHECK |
| Leading Edge -CHECK | Cargo Compartment –ITEMS SECURED |
| Air Vent -NO BLOCKAGE | Cargo Door –CLOSED |
| Upper Surface -CHECK |  |
| Lower Surface -CHECK | WINDSHIELD |
| Fuel Vent -NO BLOCKAGE | Surface -CLEAN |
| Fuel Drain -CLOSED |  |
| Landing Gear -CHECK | DOCUMENTS (A-R-R-O-W) |
| Wing Joint Seal -CHECK | Airworthiness Certificate |
|  | Registration Certificate |
| NOSE | Radio Station License |
| Oil (open oil door) –CHECK (2 QT Min., 6 QT Normal, 8 QT Max.) | Operator’s Manual (FAA Approved) |
| Cowling DOES NOT OPEN | Weight and Balance Data |
| Air Intakes -NO BLOCKAGE |  |
|  | MAINTENANCE INSPECTIONS: Complied With |